## Slide 1: FUELS
A combustible substance which on proper burning in air liberates huge amount of heat, that can be used economically for domestic and industrial purposes
e.g. coke, coal, charcoal, petroleum diesel etc

## Slide 2: Where We Get Oil?
The world's top five crude oil-producing countries are:
  Saudi Arabia
  Russia
  United States
  Iran
  China

## Slide 3: Composition of petroleum
C : 80-87%
H : 15%
S,N,O : 1%

## Slide 4
Composition of Crude Oil

## Slide 5: Fractional Distillation of Petroleum
Petroleum can be separated into different fractions by fractional distillation.
This separation can take place because petroleum is a mixture of substances with different boiling points.

## Slide 6: Conditions for Oil Refining
Petroleum is heated to 360C in the absence of air in a furnace to vaporize it before fractional distillation.

## Slide 8
Distillation to separate by boiling point ranges
Water washing to remove impurities
Conversion reactions to alter molecular structures
Mixing to obtain maximum commercial characteristics
Petroleum delivered from well field

## Slide 9: CLASSIFICATION
Fuels
Primary or natural Secondary or derived
Solid liquid Gaseous
Wood crude oil Natural gas
Coal
Dung
solid liquid gaseous
coke tar coal gas
charcoal kerosene water gas
diesel oil gas
Petrol bio gas
LPG

## Slide 10: CHARACTERISTICS OF A GOOD FUEL 1. High Calorific value 2. Low moisture contents 3. Moderate ignition temperature 4. Low ash content 5. No harmful combustion product formation 6. Moderate rate of combustion 7. low cost 8. Easy to transport

## Slide 11: Comparision between solid, liquid and gaseous fuels
Properties | Solid fuels | Liquid fuels | Gaseous fuels
Price | Cheap and easily available | Costly | Costly except natural gas
Transport and storage | easy | Transported easily though pipelines but must be stored in closed containers carefully | Transported through pipelines and are stored in leak proof tanks

## Slide 12
Combustion | slow | quick | Very fast
Fire hazards | Less risk | Greater risk | Even greater than liquid fuels
Smoke and ash | Always produced and reduces calorific value | Ash is not produced but smoke is produced | Neither ash nor smoke is produced
Calorific value | least | higher | Highest

## Slide 13: CALORIFIC VALUE 1g compound + O2 CO2 +H2O, ∆H= ? Here, ∆H = calorific value UNITS 1. Calorie: for 1g of water by 1oC 1calorie = 4.184 Joule = 4.185 x 107 ergs 2. K.Calorie: for 1 kg of water by 1oC 3. British Thermal Unit (B.Th.U.): for 1 pound of water by 1oF 4. Centigrade heat unit (C.H.U.): for 1 pound by 1oC

## Slide 14: GROSS OR HIGHER CALORIFIC VALUE (HCV) Heat evolved when a unit quantity of a fuel is completely burnt and the products of combustion are allowed to cool at room temperature. A + O2 CO2 + H2O(v) , ∆H1=x H2O(v) H2O(l) , ∆H2 = y (y = latent heat of steam) So, HCV = Total ∆H = x+ y

## Slide 15: LOWER OR NET CALORIFIC VALUE (LCV or NCV) Heat evolved when a unit quantity of a fuel is completely burnt and the products of combustion are allowed to escape at room temperature. A + O2 CO2 + H2O(v) , ∆H1=x LCV = x = HCV – latent heat of water vapors formed = HCV – 0.09 x H x 587 cal/g (where, H = % of hydrogen in the fuel)

## Slide 16: Differences between Gross and Net calorific value
S.No. | GCV | NCV
1 | The amount of heat released when unit quantity of fuel is burnt completely and the products of combustion are allowed to cool at room temperature. | The amount of heat released when unit quantity of fuel is burnt completely and the products of combustion are allowed to escape at room temp.
2 | Latent heat of condensation of steam is included | Latent heat of condensation of steam is not included
3 | It is also known as Higher Calorific Value | It is also known as Lower Calorific Value
4 | Having more value than NCV | Having lesser value than GCV

## Slide 19: CALCULATION mass of fuel taken in calorimeter = m g mass of water taken in calorimeter=Wg water equivalent of calorimeter bomb, thermometer, stirrer etc = w g Initial temp. of water in calorometer = t1 final temp. of water in calorimeter = t2 higher calorific value = HCV heat liberated by burning of fuel = m x HCV heat gained by water, calorimeter etc = (W+w)(t2-t1) heat liberated = heat gained m x HCV = (W + w)(t2-t1) HCV = (W+w)(t2-t1) cal/g or kcal/kg m

## Slide 20
Let H be the % of hydrogen in the fuel,then
LCV = HCV – 0.09H x 587 cal/g or kcal/kg
Corrections
(i) Fuse wire correction (CF) : should be subtracted.
(ii) Acid correction (CA) : should be subtracted.
(iii) Cooling correction (CC) : should be added.
So, HCV = (W + w)(t2-t1+CC)-(CA+CF) cal/g
m

## Slide 21
BOMB CALORIMETER

## Slide 22
COAL SAMPLE ANALYSIS
Proximate analysis
Ultimate analysis

## Slide 23
ANALYSIS OF COAL SAMPLE
Coal is a highly carbonaceous matter that has been formed from fossilized remains of plants under suitable conditions.
ANALYSIS- 2 types
1. PROXIMATE ANALYSIS - includes the determination of moisture, volatile matter, ash and fixed carbon
Moisture: at 110oC for an hour
% of moisture = Loss in wt. x 100
wt of coal sample

## Slide 24
(ii) Volatile matter : at 925+/- 25oC for 7 minutes
% of volatile matter = Loss of wt due to removal of volatile matter x 100
wt of coal sample taken
(iii) Ash content: at 700-750oC for half an hour
% of ash = wt of ash x 100
wt of coal sample taken
(iv) Fixed carbon = 100- % of (moisture + ash + volatile matter)
SIGNIFICANCE:
Higher % of fixed carbon Higher calorific value better fuel

## Slide 25
ULTIMATE ANALYSIS OF COAL
Includes the estimation of % of elements in the fuel
(i)Determination of C & H
C + O2 CO2
  H2 + O2 H2O
2KOH + CO2 K2CO3 + H2O
CaCl2 + 7H2O CaCl2.7H2O

## Slide 26
% of C =Increase in the wt of KOH tube x 12 x 100
Wt of coal sample taken x 44
% of H = Increase in the wt of CaCl2 tube x 2 x 100
Wt of coal sample taken x 18

## Slide 27
(ii) Determination of N: Kjeldahl method
Fuel(W g) + H2SO4 (NH4)2SO4
(NH4)2SO4 + NaOH NH3 +Na2SO4 + H2O
Known amount
of HCl
NH3 is neutralised Excess HCl
(Titrated against alkali)

## Slide 28
Mass of fuel = W g
Volume of acid used to neutralize NH3 = V ml
Normality of HCl = N
Eq. of HCl = Eq. of NH3 = Eq. of N
w = NVx14
1000
% of N = Wt of N2 x 100 = 1.4 NV
Wt of coal sample taken(1g) W

## Slide 29
DETERMINATION OF S:
S+ O2 SO2
SO2 + H2O H2SO4
% of S = wt of BaSO4 formed x 32 x 100
wt of coal sample x 233
(iv) DETERMINATION OF ASH:
by proximate analysis

## Slide 30
(V) DETERMINATION OF O:
% of O = 100 - % of (C + H + N + S + ash)

## Slide 31
OCTANE NUMBER
O.N. signifies the ignition quality of gasoline in automobile engines.
For grading gasoline(Petrol)
Isooctane = 100
n-heptane = 0
The % of isooctane present in the mixture of isooctane and n-heptane which has the same knocking property as the fuel itself.
More the octane number, better the fuel efficiency.

## Slide 32
Reasons for opting the blend of iso-octane & n-heptane:
The different hydrocarbon in gasoline:
Straight chain paraffin
Iso-paraffins
Naphthenes
Aromatics
For the same Carbon No; straight chain paraffin have lowest octane No.
Branched chain paraffin (isomers), Naphthenes have higher octane No.
Aromatic have high O.N. but their content is being restricted due to their carcinogenic nature.

## Slide 33
Carbon | Hydrocarbon | Octane No.
C6 – Straight chain | n- Hexane | 28.8
C6 – Isomer | Methyl Pentane | 73.4
C6 – Isomer | Dimethyl Butane | 91.8
C6 – Napthenes | Cyclohexane | 83
C6 – Aromatic | Benzene | 98
C7 – Paraffin | n - Heptane | 0
C7 – Isomer | Dimethyl Pentane | 88
C8 – Isomer | Iso – Octane | 100
C7 – Aromatics | Toluene | 107
Octane numbers of few hydrocarbons:

## Slide 34
Methods to increase octane number:
By adding the antiknocking agent: e.g. TEL (about 1.0-3.0 ml /gallon petrol) along with some ethylene dibromide.
By isomerisation
By alkylation
By aromatisation
By Cracking

## Slide 35
Conversion Reactions
CRACK
COMBINE
REARRANGE
THERMAL
CATALYTIC
ALKYLATION
POLYMERIZATION
REFORMIING
ISOMERIZATION
Dehydrogenation
Dehydroisomerization
Isomerization
Dehydrocyclization
Hydrocracking

## Slide 36
Catalytic Reforming – Conversion Reactions

## Slide 37
Cracking (Pyrolysis).
CH3-CH3 CH2=CH2 + H2
CH3CH2CH3 CH3CH=CH2 + H2
CH2=CH2 + CH4
CH3CH2CH2CH3 CH3CH2CH=CH2 + H2
CH3CH=CH2 + CH4
CH3-CH3 + CH2=CH2
Isomerisation.
CH3CH2CH2CH3 (CH3)3CH
(CH3)2CHCH2CH2CH3 (CH3)2CHCH(CH3)2 + (CH3)3C-CH2CH3
CH3 (CH2)6CH3 (CH3)2CH(CH2)4CH3
(ON = -19) (ON = 100)
AlCl3 / HCl / ∆
∆/-nce of air
∆/-nce of air
∆/-nce of air
AlCl3 / HCl / ∆
AlCl3 / HCl / ∆

## Slide 38
Aromatisation.
C6H14 C6H6
C7H16 C6H5CH3
C8H18 C6H5-CH2CH3 + o-xylene + m-xylene + p-xylene
* Catalysts: Cr2O3/Al2O3 or CrO3/Pt.
Oxidation.
With Cu at 200°C & 100 atm. : Alcohols.
With MnO at 200°C : Carboxylic acids.
With Mn(OAc)2 : Carboxylic acids.
With alkaline KMnO4 : Tertiary alcohols.
Catalyst / 600°C
Catalyst / 600°C
Catalyst / 600°C

## Slide 39
CETANE NUMBER
For grading diesel oil
Normal paraffin's have highest cetane no. followed by naphthenes, isoparaffins, olefins and aromatics.
For grading diesel oil.
Hexadecane (cetane) = 100
α- methyl naphthalene = 0
The % of cetane present in the mixture of cetane and α-methyl naphthalene which has the same ignition property as the fuel itself.
More the cetane number, better the fuel efficiency.

## Slide 40
FLASH POINT
The flash point of a volatile liquid is the lowest temperature at which it can vaporise to form an ignitable mixture in air.
At the flash point, the vapour may cease to burn when the source of ignition is removed.
Or
The minimum temperature, at which the sample gives sufficient vapours, which forms an ignition mixture with air, giving a flash when a flame is applied to it, is called flash point.

## Slide 41
FLASH POINT
The flash point of a volatile liquid is the lowest temperature at which it can vaporise to form an ignitable mixture in air.
At the flash point, the vapour may cease to burn when the source of ignition is removed.
Or
The minimum temperature, at which the sample gives sufficient vapours, which forms an ignition mixture with air, giving a flash when a flame is applied to it, is called flash point.

## Slide 42: CHARACTERISTICS OF SATURATED HYDROCARBONS (ALKANES)
General formula: CnH2n+2 (n is a whole number).
All the four valencies satisfied with hydrogen/carbon/any other atom.
Consist of only carbon and hydrogen bonded by single covalent bonds.
Range from Methane (one Carbon atom in the molecule) upto molecules containing 60+ C atoms i.e., a range of molecular weights from 16 upto 850 +.
Straight- or branched-chain molecules.
Rotation about single covalent bonds
occurs freely. The energy barrier is small.
The position of hydrogen atoms relative to
one is thus constantly changing.

## Slide 43
Skeletal structure of only carbon atoms
Methane Ethane Propane
n-Butane iso-Butane
C1 – C4 n-alkanes are all gases.
Methane main component of natural gas.
Propane and butane often stored as compressed gases.

## Slide 44
PREPARATION OF ALKANES
By the reduction of unsaturated hydrocarbons.
RCH=CH2 + H2 RCH2CH3
By Wurtz reaction.
2RCH2X + 2Na RCH2CH2R
From Grignard Reagent.
RMgX +H2O → RH + Mg(X)OH
Kolbe’s electrolytic method.
2RCOONa 2RCOO- + 2Na+
(At anode) (At cathode)
2Na+ 2Na 2NaOH + H2
2RCOO- 2RCOO˙ 2R˙ R-R
Ni
Current
-2e-
+2e-
H2O
Coupling
-2CO2
Ether / ∆

## Slide 45
From sodium salt of carboxylic acids.
RCOOH + NaOH → RCOONa + H2O
RCOONa RH + Na2CO3
By the reduction of alkyl halides.
RI RH + I2
RI RH + I2
By the hydroboration of alkenes.
RCH=CH2 RCH2CH3
Corey-House Synthesis.
RCl + 2Li RLi + LiCl
2RLi + CuCl → R2CuLi + LiCl
R2CuLi RR’ + RCu + LiCl
HI, P
HI, P
B2H6 / THF / Propionic acid (reflux)
Ether
R’X
Soda lime

## Slide 46
PHYSICAL PROPERTIES OF ALKANES
Lower members gases, in-between liquids and higher waxy solids.
Non-polar in nature, less denser than water.
Immiscible with water making two layers but soluble in organic solvents.
Regular increases in boiling and melting points with molecular weight.
Specific gravity increases with increase in molecular weight.

## Slide 47
CHEMICAL PROPERTIES OF ALKANES
Combustion.
CnH2n+2 + (3n+1/2) O2 → (n+1) H2O + nCO2
Free radical substitution reactions.
Nitration.
RCH2R’ + HNO3 RNO2 + R’CH2NO2 + R’NO2 + RCH2NO2 + RCH(NO2)R’
Halogenation.
CH4 CH3Cl CH2Cl2 CHCl3 CCl4
Sulfonation.
RH + H2SO4 → RSO3H + H2O
450°C
Cl2/UV light
Cl2/UV light
Cl2/UV light
Cl2/UV light

## Slide 48
CHARACTERISTICS OF
UNSATURATED HYDROCARBONS
    General formula CnH2n.
    Presence of double or triple bonds in between different carbon atoms.
    Straight or branched chain molecules.
    sp2 hybridized.
    Trigonal planar in shape.

## Slide 49
PREPARATION OF ALKENES
By the dehydration of alcohols.
C2H5OH CH2=CH2 + H2O
CH3CH2CH2OH CH3CH=CH2 + H2O
(CH3)3COH (CH3)2C=CH2
(*Elimination according to Saytzeff’s rule).
By the dehydrohalogenation of alkenes.
CH3CH2Br CH2=CH2 + Br- + H2O
By the dehalogenation of vicinal dihalides.
CH2Br-CH2Br CH2=CH2 + ZnBr2
H2SO4 / 160°C
Alc. KOH / ∆
H2SO4 / 180°C
H2SO4 / 85°C
Zn / CH3COOH

## Slide 50
By Cracking.
CH3-CH2-CH2-CH3 CH4 + CH2=CH-CH3
CH2=CH2 + CH3CH3
By the controlled hydrogenation of alkynes.
RC≡CH + H2 RCH=CH2
Pd-CaCO3 / quinoline
∆

## Slide 51
PHYSICAL PROPERTIES OF ALKENES
First three members: gases at ordinary temperature; next fourteen liquids; rest solids.
Slightly soluble in water; freely soluble in organic solvents.
M.P., B.P. and specific gravity rise with increase in molecular weight.

## Slide 52
1. ADDITION REACTIONS
Alkyl Halides
Alkyl hydrogen Sulfate
Alcohols
Dihaloalkanes
Addendum

## Slide 53
Mechanism of Addition reactions on C=C
Ionic mechanism. Always Electrophilic addition
*The electrophile is a Lewis acid, i.e. it accepts a pair of electrons,
while nucleophile is a Lewis base, its donated a pair of electrons.
Step I: Attack of electrophile
Step II: Attack of nucleophilic part of the addendum.
The Slow Step is the Rate Determining Step

## Slide 54
Anti-Markovnikov’s Rule / Peroxide Effect / Khharasch Effect: Addition reversed in the +nce of peroxides.
CH3CH2CH2Br
CH3-CH=CH2 + HBr
CH3CHBrCH3
(*Proceeds via free radical mechanism).
Markovnikov’s Rule:
+ve part of the addendum goes to that carbon atom which already contains the maximum number of H atoms.
Unsymmetrical Alkene
No peroxide
Peroxide

## Slide 55
(i) Addition of sulfuric acid

## Slide 56
2o Carbocation prefered
1o Carbocation
3o > 2o > 1o
Carbocation stability
2-Bromopropane
(Major product)
1-Bromopropane (Minor product)
(ii) Addition of Halogen acids

## Slide 57
(iii) Bromination
Back-side nucleophilic attack of bromide ion: opening of three membered ring.
*Stereospecific Product
Formation of cyclic intermediate.

## Slide 58
(v) Addition of Hypohalous acid.
CH2=CH2 + HOX → HOCH2-CH2X
Halohydrin

## Slide 59
(iv) With Ozone: Aldehydes and ketones.
R2C=CHR R2CO + RCHO
RCH=CHR’ RCOOH + R’COOH
3. Combustion.
CH2=CH2 + 3O2 → 2CO2 + 2H2O
4. Polymerisation:
O3 / Zn-H2O
Large molecules containing many identical repeating units (100- 1000000).
Condensation Polymerisation: A by-product is eliminated along with the formation of polymer.
Addition polymer: Monomer simply add together to give the polymer without elimination of by-product.
O3 / H2O2

## Slide 61
General formula CnH2n-2.
Presence of triple bond, containing one σ and two Π-bond.
The two p-bonds are perpendicular to each other and form a cylinder of negative charge about the axis of the bond ---------- No bond rotation about triple bond.
sp-orbitals contain 50% s- and 50% p-character.
The carbon-carbon bond is 1.2Ao shorter than C=C, which is 1.3Ao. C-H bond is also shorter than ethene, which is shorter than ethane.
The bonding electrons reside closer to the C-nucleus, and so are held more tightly.
CHARACTERISTICS OF ALKYNES

## Slide 62
PREPARATION OF ALKYNES
From calcium carbide:
CaC2 + 2H2O → HC≡CH + Ca(OH)2
2. From dehydrohalogenation of vicinal dihalides:
CH3CHBrCH2Br + 2KOH → CH3C≡CH + 2KBr + 2H2O
RCH2CHBrCH2Br + 2NaNH2 RCH2C≡CH + 2NaBr + 2NH3
(*KOH helps in isomerisation).
3. From ketones.
RCOCH2R’ RC(X2)CH2R’ RC≡CR’ + 2HCl
4. By the displacement reaction.
RC≡CH RC≡C-Na+ RC≡CR’ + NaX
150°C
Alc. KOH
PX5
NaNH2
R’X

## Slide 63
PHYSICAL PROPERTIES OF ALKYNES
First three members gases; next eight liquids; higher solids.
Slightly soluble in water; soluble in organic solvents.
B.P., M.P., density increase with increase in molecular weight.

## Slide 64
CHEMICAL PROPERTIES OF ALKYNES
1. Addition reactions:
Reduction.
RC≡CH RCH=CH2 RCH2CH3
R R
RC≡CR C=C
H H
cis-alkene
R H
C=C
H R
trans-alkene
Alkynes are more reactive in halogenation reactions than alkenes.
H2, Ni
H2, Ni
H2, Pd / BaSO4
Quinoline
Na / NH3

## Slide 65
(ii) Addition of Halogens.
RC≡CR RCX=CXR RCX2-CX2R
(iii) Addition of Hydrogen Halides.
RC≡CH RCX=CH2 RCX2CH3
2. Addition of HCN.
HC≡CH + HCN CH2=CHCN
X2 / CCl4
X2 / CCl4
HX (g)
HX (g)
CuCl in HCl

## Slide 66
4. Reaction with metals.
RC≡CH + NaNH2 → RC≡C-Na+ + NH3
RC≡C-Na+ + R’Br → RC≡CR’ + NaBr
RC≡CH + AgNO3 + NH4OH → RC≡CAg + H2O + NH4NO3
2RC≡CH + Cu2Cl2 + 2NH4OH → 2RC≡CCu + 2H2O + 2NH4Cl
RC≡CH + CH3MgBr → RC≡CMgBr + CH4

## Slide 67
ALICYCLIC COMPOUNDS / NAPHTHENES
Cyclic and aliphatic in nature.
General formula CnH2n (n is a whole number usually from 1 to 20).
Isomeric with alkenes.
Ring structures are monocyclic to Polycyclic combinations.
Cyclopropane
Cyclobutane
Cyclopentane

## Slide 68
PREPARATION OF CYCLOALKANES
By the reaction of dihalogen derivatives with sodium.
XCH2-CH2-CH2X + 2Na → + 2NaX
2. By the photolysis of cyclic ketones.
+ CO
3. By Clemmensen or Wolf-Kishner reduction.
4. By the reduction of aromatic hydrocarbons.
hυ
Zn -Hg/ HCl
NH2NH2 / KOH
H2 / Ni

## Slide 69
PHYSICAL PROPERTIES
First two members gases, rest liquids.
M.P., B.P. increase with increase in molecular weight.
Insoluble in water, soluble in organic solvents.

## Slide 70
CHEMICAL PROPERTIES OF CYCLOALKANES
Ring Opening reactions.
CH3CH2CH3
BrCH2CH2CH2Br
CH3CH2CH2Br
CH3CH2CH3
2. Substitution reactions. X
+ X2 + HX
H2, Pd / C
Br2
HBr
H2, Ni , ∆
hυ

## Slide 71
AROMATICS
General formula: C6H5-Y (Y is a longer, straight molecule that connects to the benzene ring).
Ringed structures with one or more rings.
High carbon content: burns with smoky flame.
Cyclic.
Conjugation.
Planar structure.
Resonance.
Follow Huckel’s rule [Cyclic cloud of π-electrons with presence of (4n+2) π- electrons].
Show saturated behaviour.

## Slide 72
PREPARATION OF AROMATIC HYDROCARBONS
By heating the sodium salt of aromatic carboxylic acid in the +nce of soda-lime.
C6H5COONa C6H6 + Na2CO3
By Friedel-Craft’s alkylation.
C6H6 + RX C6H5R
Aromatization.
Soda-lime / ∆
AlCl3 / reflux
C6H14 C6H6
C7H16 C6H5CH3
C8H18 C6H5-CH2CH3 + o-xylene + m-xylene + p-xylene
Catalyst / 600°C
* Catalysts: Cr2O3/Al2O3 or CrO3/Pt.
Catalyst / 600°C
Catalyst / 600°C

## Slide 73
CHEMICAL PROPERTIES OF AROMATIC HYDROCARBONS
Reactivity is different to other unsaturated compounds- Substitution rather than Addition is favoured.
Substitution reactions: Electrophilic substitution.
C6H6 + E-Nu → C6H5-E + HNu
Halogenation.
C6H6 + X2 C6H5X + HX
(ii) Nitration.
C6H6 C6H5NO2
(iii) Sulfonation.
C6H6 C6H5SO3H
anhy. AlCl3
Conc. HNO3 / Conc. H2SO4
Conc. H2SO4

## Slide 74
(iv) Friedel-Craft;s reaction.
Alkylation.
C6H6 + RX C6H5R + HX
B. Acylation.
C6H6 + RCOX C6H5COR + HX
C6H6 + (RCO)2O C6H5COR + RCOOH
anhy. AlCl3
anhy. AlCl3
anhy. AlCl3

## Slide 75
1k.cal = 1000Cal = 3.968 B.Th.U. = 2.2 C.H.U.